## Slide 1: SHEGA – Smart Home Environmental Guardian Assistant
CO₂, CO & Smoke Monitoring + Stove Safety
Sebah Tewodros Tesfatsion| IoT Project | 2025

## Slide 2: Problem Statement
Why Shega
Poor indoor air quality (CO₂, CO, smoke, particulate matter)
Cooking-related hazards (overheating stoves, fires)
Checking stove status online

## Slide 3: Project Objectives
- Real-time indoor air quality monitoring
- Stove safety management with actuators (buzzer + fan)
- Centralized dashboard for control & visualization
- Data logging (MongoDB )
- AI-powered assistant

## Slide 4: System Components
- AirNode (CO₂, CO, PM, Temp, Humidity, Buzzer)
- StoveNode (Thermocouple, LED, Fan)
- MQTT Broker (HiveMQ)
- Node.js + Express Server
- MongoDB Database
- Dashboard ( Next.js + recharts)
- RAG Assistant (Python + Flask +TF-IDF +Phi-3 Min)

## Slide 5: Edge Devices
- AirNode: ESP32 + DHT22 + SCD30 (CO₂) + ZE03-CO (CO) + PMS5003 (PM)+Buzzer
- StoveNode: ESP32 + Thermocouple (MAX31855)+ Fan
- Simulated via WokWi or/and Node.js
- Identified with Home ID + Device ID

## Slide 6: Communication Layer
- MQTT Protocol with Mosquitto broker
- Example topics:
• shega/airnode/data → sensor readings
• shega/stovenode/status → stove state
• shega/stovenode/control → actuators
• shega/alerts → emergencies
- Secure broker with username/password

## Slide 7: Backend & Data Management
- Node.js + Express REST API
- Functions:
• Receive MQTT messages
• Save telemetry in MongoDB
• Provide APIs for dashboard
• Trigger alerts
- Data stored in JSON

## Slide 8: Dashboard
- User Views:
• Real-time gauges (CO₂, CO, PM, Temp)
• Stove status & control
• Historical charts
• - Admin Views:
• All houses + all devices
- Built with Next.js + recharts

## Slide 9: Powered RAG Assistant
Bilingual RAG Assistant – answers in Amharic & English
Combines telemetry + knowledge base for context
TF-IDF + cosine similarity for fast document retrieval
Local LLM via Ollama (Phi-3 Mini / TinyLlama / Llama2) for generation
Flask API + Next.js dashboard with live streaming responses
Knowledge Base: JSON (100+ entries)

## Slide 10: UX flow
Data flow

## Slide 11: Implementation Details
- Technologies:
• Arduino (ESP32, WokWi)
• Node.js + Express
• Next js Dashboard
• MongoDB
• MQTT (HiveMQ)
• Python (RAG)
- Simulation: WokWi + Node.js device simulators

## Slide 12: Demo / Screenshots
- MQTT topics in action
- Dashboard gauges
- Admin multi-house view
- RAG assistant answers )

## Slide 13: Challenges & Solutions
- WokWi doesn’t support all sensors → Node.js simulators
- Secure MQTT connection → Broker authentication
- RAG assistant irrelevant answers → Improved prompt + intent detection

## Slide 14: Future Improvements
- Mobile app integration
- SMS/Telegram alerts
- More sensors (VOC, formaldehyde)
- Smart appliance integration

## Slide 15: Conclusion
- SHEGA provides:
• Safer kitchens
• Indoor air monitoring
• Bilingual user education
- Meets IoT project requirements (devices, sensors, actuators, MQTT, dashboard, AI)

## Slide 16: Q&A
Thank you!
Any Questions?